## Slide 1: Indoor State Estimation
With MarvRx Inc
Chinemelu Ezeh, Oskar Weigl, Thomas Morris, Ryan Savitski and Josh Eldson

## Slide 2: Project Aim
Solve the localisation problem of Autonomous Systems in GPS denied environment.
Important application in Aerial Photography and Pipeline Surveillance.
Offer a cheap solution

## Slide 3: Who are Mavrx Autonomy?
Start-up company in autonomous aerial vehicles for high definition imaging.
Secured £500,000 in kick-starter funding.

## Slide 4: Presentation Overview
High Level Design
  Feature Extraction, State Estimation
Low level design
  Floodfill, System Model Derivation
Demonstration
Commercialisation

## Slide 5: Solution Overview
Robot moves around in the room increasing its location uncertainty.
It observes features with need to be added to its internal map
It re-observes these features and makes corrections to adjust its localisation.

## Slide 6: High Level Design
Feature Extraction
  We use planes as landmarks extracted using Floodfill algorithm and Xtion Pro RGB-D camera
State Estimation
  We employ the Extended Kalman Filter Algorithm to estimate quad’s state.

## Slide 7: How Depth Camera Works
Xtion uses an infrared projector and sensor.
Depth map (left) is reconstructed from the light coding of the image(right).
Techniques used include analysis of parallax and analysis of blur.

## Slide 8: Feature Extraction
We extract planes using Point Cloud Library and Flood fill algorithm.
Xtion Pro camera produces depth information for pixels.
We use this to estimate equation of local plane.
Group locals into cluster.

## Slide 9: Feature Extraction(DBSCAN)

## Slide 10: State Estimation
Using the Extended Kalman filter we track:
  Position
  Speed
  Attitude(Yaw, Pitch, Roll)
We model our system using inertial sensor data and do not use a physical model of the quadcopter.

## Slide 11: Kalman Filter Algorithm
Pk-1|k-1
xK-1|k-1
Prior State Knowledge
Prediction step based on motion model
Pk|k-1
xK|k-1
Update step
Compare prediction to measurement
Measurements
Extracted features/ Planes
Pk|k
xK|k
Next timestep
K ←K+1
Output estimate of state

## Slide 12: Mathematics of Kalman Filter
Predict Stage
  Predicted state estimate
  Predicted covariance
Update Stage
  Innovation residual
  Innovation residual covariance
  Optimal Kalman Gain
  Update state estimate
  Update Covariance Estimate

## Slide 13: Demonstration

## Slide 14: Commercialisation
Unmanned Aerial Vehicle(UAV) Applications
  Security: Border Control, Disaster Monitoring.
  Civilian: Aerial Photography, Pipeline Surveillance.
  Europe to spend over £1billion on UAVs from 2008 to 2015.

## Slide 15: Market Breakdown

## Slide 16: Summary & Conclusion
  We were able to provide a proof of concept to the localisation problem
  Localisation is a first step towards full autonomy.
  Autonomous Quadcopters are very useful in border control, aerial photography, etc.
  Our solution consists of plane extraction using DBScan and Extended Kalman filter for estimation.

## Slide 17: References
  http://www.barnardmicrosystems.com/L4E_uav_market.htm
  More Information on Our R10 quadcopter
    https://r10plus.uair.co/r10