## Slide 1: Indoor State Estimation
With MarvRx Inc
Chinemelu Ezeh, Oskar Weigl, Thomas Morris, Ryan Savitski and Josh Eldson

## Slide 2: Project Aim
Solve the localisation problem of Autonomous Systems in GPS denied environment.
Important application in Aerial Photography and Pipeline Surveillance.
Offer a cheap solution

## Slide 3: Who are Mavrx Autonomy?
Start-up company in autonomous aerial vehicles for HD imaging.
Secured £500,000 in kick-starter funding.

## Slide 4: Presentation Overview
High Level Design
  Feature Extraction, State Estimation
Low level design
  Dbscan, System Model Derivation
Demonstration
Commercialisation

## Slide 5: High Level Design
Feature Extraction
  We use planes as landmarks extracted using Dscan algorithm and Xtion Pro RGB-D camera
State Estimation
  We employ the Extended Kalman Filter Algorithm to estimate quad’s state.

## Slide 6: Feature Extraction(DBSCAN)
We extract planes using Density Based Spatial Clustering Algorithm.
Xtion Pro camera produces depth information for pixels.
We use this to estimate equation of local plane.
Group locals into cluster.

## Slide 7: Feature Extraction(DBSCAN)

## Slide 8: State Estimation
Using the Extended Kalman filter we track:
  Position
  Speed
  Attitude(Yaw, Pitch, Roll)
We model our system using inertial sensor data and do not use a physical model of the quadcopter.

## Slide 9: Kalman Filter Algorithm
Pk-1|k-1
xK-1|k-1
Prior State Knowledge
Prediction step based on motion model
Pk|k-1
xK|k-1
Update step
Compare prediction to measurement
Measurements
Extracted features/ Planes
Pk|k
xK|k
Next timestep
K ←K+1
Output estimate of state

## Slide 10: Mathematics of Kalman Filter
Predict Stage
  Predicted state estimate
  Predicted covariance
Update Stage
  Innovation residual
  Innovation residual covariance
  Optimal Kalman Gain
  Update state estimate
  Update Covariance Estimate

## Slide 11: Commercialisation
Unmanned Aerial Vehicle(UAV) Applications
  Security: Border Control, Disaster Monitoring.
  Civilian: Aerial Photography, Pipeline Surveillance.
  Europe to spend over £1billion on UAVs from 2008 to 2015.

## Slide 12: Market Breakdown

## Slide 13: Market Barriers
High Cost
Radio Spectrum
Viable Alternatives
Aviation Regulations
Public Concern
Insurance

## Slide 14: Demonstration

## Slide 15: Summary & Conclusion
  We were able to provide a proof of concept to the localisation problem
  Localisation is a first step towards full autonomy.
  Autonomous Quadcopters are very useful in border control, aerial photography, etc.
  Our solution consists of plane extraction using DBScan and Extendend Kalman filter for estimation.

## Slide 16: References
  http://www.barnardmicrosystems.com/L4E_uav_market.htm